## Slide 1: Image Signal Processor (ISP)
Abdul Moiz Sheikh

## Slide 2: Contents
Types by architecture
  Inline
  Offline
Types of Processing
  Bayer Domain
  RGB Domain
  YUV Domain

## Slide 3: Types by architecture
Inline Architecture
  Sensor Transfers the data directly to the ISP
  ISP processors the data
  Resulting enhanced image saved in memory
  ISP needs to be able to process data as it comes in
  Faster as compared to Offline architecture
Offline Architecture
  Sensor Transfers the data to the memory
  ISP processors the data from memory
  Resulting enhanced image saved in memory
  ISP does not need to process data as it comes in
  Sloweras compared to Inline architecture

## Slide 4: Types Of Processing
Bayer Domain Processing
    Dead Pixel Correction
    Black Level Compensation
    White Balance Gain Control
    Color Filter Array Interpolation
RGB Domain Processing
    Color Correction Matrix
    Color Space Conversion
YUV Domain Processing
    Edge Enhancement

## Slide 5: Bayer Domain
Color Images require three basic frames (Red, Green, Blue) to form color images.
Sensors are constrained by bandwidth of raw data transfer
To mitigate this issue sensors transfer data according to Bayer Pattern as shown in figure.
The Missing values for each channel are interpolated.

## Slide 6: Bayer Domain Processing
Dead Pixel Correction
  Arises due to manufacturing Defects in sensors
  Can be also due to Sensing environment
  Can be Classified as
    Static
    Dynamic
  Static Defects removed by storing location and correction factor
  Dynamic Defects can be corrected by interpolation or gradient based correction.

## Slide 7: Bayer Domain Processing
Black Level Correction
  Arises due to the fact that voltage for zero level (Black) is not exactly zero, resultantly black pixels are not purely black.
  Can be corrected by subtracting a prefixed offset from the individual pixel.

## Slide 8: Bayer Domain Processing
White Balance Gain Control
  When using Bayer's pattern a overcast of green red or blue is created in parts of image which are supposed to be pure white.
  Can be corrected by using following formulae

## Slide 9: Bayer Domain Processing
Color Filter Array Interpolation
  Used to fill in the empty spaces in each channel by interpolation. This converts the image from Bayer's domain to RGB domain.
  Can be implemented using a convolution of a 5x5 matrix with image
  Different kernels used for each channel, out of 8 possible kernels , can also be used one after the other.

## Slide 10: RGB Domain Processing
Color Correction Matrix
  Color Images have difficulty in accurately reproducing Color due to lens, filter, light sourcing defects etc.
  Can be corrected using color correction matrix.

## Slide 11: RGB Domain Processing
Color Space Conversion
  Used to convert from RGB domain to YCbCr domain.
  Can be of one of three types depending on the quality of result image required.
  Conversion to BT.2020 standard used to UHDTV is given below

## Slide 12: YUV Domain Processing
Edge Enhancement
  Used to enhance edges of different objects and sharpen the edges.
  Works by increasing the contrast around the edges of the objects.
  A sample edge detection matrix in Y channel is shown below.

## Slide 13: Possible Pipeline for ISP